## Slide 1: Embedded Systems
University Course
NXP

## Slide 2
Alex Cuhureanu
Bio:
  SW developer for over 7 years in NXP where I am developing software for an Integrated Development Environment named S32Design Studio.
  Java, Maven, Jenkins, GIT, C/C++
Topics covered in this course:
  V-Model/Requirements
  Virtual Machine Environment Setup
  Process | Git, IDE Setup, Compile and Flash the Hello World Project
  How Hardware and Software are Linked
  Lights Node
  Review and Exercises

## Slide 3
Ramona Dragulin
Bio:
  SW developer in System Tools department where I am developing software for an Integrated Development Environment named S32Design Studio.
  Java , Maven, Python, C++ to implement S32DS.
Topics covered in this course:
  Process | Git, IDE Setup, Compile and Flash the Hello World Project
  Architecture (UML) | Virtual Machine Environment Setup
  RGB | Hands-on Lab (no module – just the dev board)
  Brakes Node
  Review and Exercises

## Slide 4: A smarter world starts with NXP
We design purpose-built, rigorously tested technologies that enable devices to sense, think, connect and act intelligently to improve people's daily lives.
Corporate Overview
Communication Infrastructure
Smart City
Smart Home
Automotive
Industrial & IoT
Mobile

## Slide 5: Ground RULES
There are no stupid questions!
Please be respectful to your colleagues
If you need to go to the bathroom, take a phone call, or take a small break you do not need to ask permission, just leave without disturbing
Please interrupt me at any time during my presentation if you want to ask questions
Please tell me if I am going too fast or too slowly
The goal of this event is for you to understand the basic concepts, it is not for me to go through everything I have prepared
One big break from 12pm to 1pm for lunch
We will have small breaks that we can agree on

## Slide 6: Course Contents
General topics, Courses & Labs
General Presentation of the Course
V-Model, Requirements Engineering, Process | Understand and Create Requirements
Process | Git, IDE Setup, Compile and Flash the Hello World Project
Architecture (UML) | Virtual Machine Environment Setup
How Hardware and Software are Linked | From Compiling to Electrical Signals and Debugging
RGB | Hands-on Lab (no module – just the dev board)
Node 1: Brake
Node 2: Lights
Review and Exercises

## Slide 7: REPLI-CAR NETWORK
lIGHTS
brake
brake control node
Replicate Brake Control Module behavior
· brake actuation and brake lamp indication based on input controller from HMI
· Communications with other nodes: HMI, PCM, BCM
LIGHTS control node
Replicate Body Control Module behavior
· Actuate lights (headlamps, turn indicators), horn and washer pump based on input controller from HMI
· Communications with other nodes: HMI, PCM, Brake, Steering, Comfort

## Slide 8: V-Model

## Slide 9: The V-MODEL
Known as verification and validation model
It is similar to waterfall model that follows a sequential path of execution of processes
Devised by the late Paul Rook in 1980s, V-model was targeting the improvement of software development
It is a step-by-step process in which the next phase begins only after the completion of the present phase
If this model is used to test a product, there is an assurance that the final product developed will be of high quality
Coding
Unit Test
Model Design
Integration Test
Architecture Design
System Test
System Design
Acceptance Test
Requirements Design

## Slide 10: Phases of V-Model – Verification phase
The verification phase of V-model includes:
Business requirement analysis is the stage of having a detailed communication with the customer so that it gets easier to understand his/her exact requirements.
System design stage involves understanding and detailing out the entire hardware and communication setup for the product being developed. System test design can also be planned at this stage
Architectural design stage involves understanding the technical and financial feasibility of the product before it is actually developed. The focus is to understand the data transfer that will take place between internal and external modules
Module design stage focuses on designing a detailed plan for the internal modules of the system. Also known as low-level design, it is important to ensure that the design is compatible with other modules in system architecture and other external systems
Notes: Business requirement: It is beneficial to complete acceptance test design planning at this stage

## Slide 11: Phases of V-Model – CODING phase
During this phase, the actual coding of the system modules is taken up
On the basis of system and architectural requirements of the program, the best suitable programming language is selected using which the coding is done at par with the coding guidelines and standards; the code is then reviewed and optimized to ensure the delivery of best performing product

## Slide 12: Phases of V-Model – Verification phase
During this phase, the product undergoes various forms of testing.
Unit testing is conducted at an early stage so that the bugs are eliminated at the starting stages of product development
Integration testing is done to check whether there is a valid and proper communication within the internal modules of the system
System testing enables the testing of the entire system and to ensure if the internal modules communicate effectively with the external systems
Acceptance testing is done to test a product in the user’s environment and to check if it’s compatible with the other systems available in the environment

## Slide 13: Requirements Engineering

## Slide 14: What is requirements engineering?
Notes: When a customer describes what s/he wants, it tends to be true that s/he always overstates it.
The product owner gathers the customer's requirement and summaries it.
Engineers follow PO's summary and make it work. Well, to some extent...
Then programmers will write it. However, when you test it, it is not workable.
Finally, we have a product, so the sales can start their job by exaggerating its features.
When you want to check the document, it is always nowhere to be found.
What the operations build is simply a rope. Gosh, I don't know what to say.
Customers are billed for extraordinary experiences.
The way Helpdesk solves problems is just simple and "radical".
Voila! It turns out what the customer truly wants is just a simple tire swing.

## Slide 15: What is requirements engineering?
Requirements Engineering (RE) is the process of discovering, analyzing, documenting and validating the requirements of the system
Each software development process goes through the phase of requirements engineering
The processes used for RE vary widely depending on the application domain, the people involved and the organization developing the requirements

## Slide 16: Requirements engineering – Problems of requirements analysis
Stakeholders don’t know what they really want
Stakeholders express requirements in their own terms
Different stakeholders may have conflicting requirements
Organizational and political factors may influence the system requirements
The requirements change during the analysis process.
New stakeholders may emerge and the business environment change

## Slide 17: The requirements analysis process
Domain Understanding
Requirements Collection
Classification
Conflict Resolution
Prioritization
Requirements Validation
Requirements Definition and Specification

## Slide 18: Process activities & Viewpoint-oriented elicitation
Process activities:
  Domain understanding
  Requirements collection
  Classification
  Conflict resolution
  Prioritization
  Requirements checking
Viewpoint-oriented elicitation:
  Stakeholders represent different ways of looking at a problem or problem viewpoints
  This multi-perspective analysis is important as there is no single correct way to analyze system requirements

## Slide 19: Requirements validation
Validation
  Concerned with demonstrating that the requirements define the system that the customer really wants​
  Requirements error costs are high, so validation is very important​
  Fixing a requirements error after delivery may cost up to 100 times the cost of fixing an implementation error​
Requirements management is the process of managing changing requirements during the requirements engineering process and system development​
  Requirements are inevitably incomplete and inconsistent​
  New requirements emerge during the process as business needs change and a better understanding of the system is developed​
  Different viewpoints have different requirements and these are often contradictory​

## Slide 20: Enduring and volatile requirements
Enduring requirements
  Stable requirements derived from the core activity of the customer organization. E.g. a hospital will always have doctors, nurses, etc. May be derived from domain models
Volatile requirements
  Requirements which change during development or when the system is in use. In a hospital, requirements derived from health-care policy

## Slide 21: Writing Good Requirements
A good requirement states something that is necessary, verifiable, and attainable.
  Need. If there is a doubt about the necessity of a requirement, then ask: What is the worst thing that could happen if this requirement were not included? If you do not find an answer of any consequence, then you probably do not need the requirement.
  Verification. As you write a requirement, determine how you will verify it.
  Attainable. To be attainable, the requirement must be technically feasible and fit within budget, schedule, and other constraints.
  Clarity. Each requirement should express a single thought, be concise, and simple. It is important that the requirement not be misunderstood – it must be unambiguous.
Simple sentences will most often suffice for a good requirement.
Notes: A good requirement states something that is necessary, verifiable, and attainable.
Even if it is verifiable and attainable, and eloquently written, if it is not necessary, it is not a good requirement. To be verifiable, the requirement must state something that can be verified by examination, analysis, test, or demonstration. Statements that are subjective, or that contain subjective words, such as "easy", are not verifiable. If a requirement is not attainable, there is little point in writing it. A good requirement should be clearly stated.
Need. If there is a doubt about the necessity of a requirement, then ask: What is the worst thing that could happen if this requirement were not included? If you do not find an answer of any consequence, then you probably do not need the requirement.
Verification. As you write a requirement, determine how you will verify it. Determine the criteria for acceptance. This step will help ensure that the requirement is verifiable.
Attainable. To be attainable, the requirement must be technically feasible and fit within budget, schedule, and other constraints. If you are uncertain about whether a requirement is technically feasible, then you will need to conduct the research or studies to determine its feasibility. If still uncertain, then you may need to state what you want as a goal, not as a requirement. Even if a requirement is technically feasible, it may not be attainable due to budget, schedule, or other, e.g., weight, constraints. There is no point in writing a requirement for something you cannot afford -- be reasonable.
Clarity. Each requirement should express a single thought, be concise, and simple. It is important that the requirement not be misunderstood -- it must be unambiguous. Simple sentences will most often suffice for a good requirement.

## Slide 22: Writing Good Requirements - Use of terms
In a specification, there are terms to be avoided and terms that must be used in a very specific manner. Authors need to understand the use of shall, will, and should:
  Requirements use shall
  Statements of fact use will
  Goals use should.
These are standard usage of these terms. You will confuse everyone if you deviate from them. All shall statement (requirements) must be verifiable, otherwise, compliance cannot be demonstrated.
Terms such as are, is, was, and must do not belong in a requirement. They may be used in a descriptive section or in the lead-in to a requirements section of the specification.
There are several terms to be avoided in writing requirements, because they confuse the issue and can cost you money, e.g.: support, but not limited to, etc., and/or

## Slide 23: Writing Good Requirements - Use of terms
The word support is often used incorrectly in requirements. Support is a proper term if you want a structure to support 50 pounds weight. It is incorrect if you are stating that the system will support certain activities.
  WRONG: The system shall support the training coordinator in defining training scenarios.
  RIGHT: The system shall provide input screens for defining training scenarios. The system shall provide automated training scenario processes.
The terms but not limited to, and etc. are put in place because the person writing the requirements suspects that more may be needed than is currently listed. Using these terms will not accomplish what the author wants and can backfire.

## Slide 24: Writing Good Requirements – Structure/grammar
Requirements should be easy to read and understand. The requirements in a system specification are either for the system or its next level (e.g.: subsystem). Each requirement can usually be written in the format:
  The System shall provide …
  The System shall be capable of...
  The System shall weigh...
  The Subsystem #1 shall provide ...
  The Subsystem #1 shall interface with...
Note: The name of your system and the name of each subsystem appear in these locations. If you have a complex name, please use the acronym, or your document will have many unneeded pages just because you have typed out a long name many times

## Slide 25: Writing Good Requirements – Structure/grammar
Each of these beginnings is followed by what the System or Subsystem shall do.
Each should generally be followed by a single predicate, not by a list.
Requirement statements should not be complicated by explanations of operations, design, or other related information. This non-requirement information should be provided in an introduction to a set of requirements or in rationale.
You can accomplish two things by rigorously sticking to this format:
  First, you avoid the Subject Trap.
  Second, you will avoid bad grammar that creeps into requirements when authors get creative in their writing

## Slide 26: Writing Good Requirements – Structure/grammar - Bad grammar
Bad grammar → reader will misinterpret what is stated.
Avoid it by writing requirements as bullet charts. When the content is agreed upon a good writer can convert the information into a sentence for the specification.
Authors will also try to put all that they know in a single sentence. This results in a long complex sentence that probably contains more than one requirement. Bullet charts or one good editor can alleviate this problem.

## Slide 27: Writing Good Requirements – Verifiable
Requirements may be unverifiable for several reasons. The following discusses the most common reason: use of ambiguous terms – because they are subjective (different meanings to different people).
Avoid these words:
  Minimize / Maximize
  Rapid
  User-friendly
  Easy
  Sufficient
  Adequate
  Quick

## Slide 28: Requirements Brakes
Inlocuitor pedala frana -> sensor de presiune
ADC – senzorul de presiune
Banda LED pentru a afisa intensitatea apasarii

## Slide 29: Requirements Lights
Faza lunga
  2 LED-uri
  1 buton
Faza scurta
  2 LED-uri
  1 buton
  Intensitatea mai mica decat la faza lunga
Faza lunga nu poate fi pornita fara faza scurta
Butoane pentru activare
Semnalizari
  4 LED-uri(stanga si dreapta, culoare galbena)
  2 butoane (stanga si dreapta)
Stopuri
  1 buton
  2 LED-uri – culoare rosu

## Slide 30: References

## Slide 31: References
Ian Sommerville, Software Engineering (International Computer Science Series), 22 Aug. 2000
Writing Good Requirements, https://spacese.spacegrant.org/uploads/Requirements-Writing/Writing%20Good%20Requirements.pdf
IEEE Guide for Developing System Requirements Specifications , https://www2.seas.gwu.edu/~mlancast/cs254/IEE_STD_1233-_Requirements_Spec.pdf

## Slide 32: Overview of the change management process
Change/Feature/Bug Requests, Implementation (Coding), Review, Branch, Commit, PullRequest, Testing

## Slide 33: Introduction in CHANGE MANAGEMENT PROCESS
The change management process refers to the stages involved in any change management strategy and its implementation. Having a strategy and steps helps transformations become successful and ensure that all factors are considered.
At a glance, the change management process breaks down into the following five steps:
1. Prepare for change.
2. Create a vision for change.
3. Implement changes.
4. Embed and solidify changes.
5. Review and analyze.

## Slide 34: Introduction in Jira
What Is Jira?
Jira is a software application developed by the Australian software company Atlassian that allows teams to track issues, manage projects, and automate workflows.
Jira is based on four key concepts: issue, project, board, and workflow.

## Slide 35: Simple schema
Jira Implementation Workflow

## Slide 36: Change request flow
Jira Implementation Workflow

## Slide 37: Support Tools Jira, Git, Bitbucket

## Slide 38: JIRA
Log-in using Windows credentials
What can you do in Jira:
  Plan and track several types of activities like tasks, sub-tasks, bugs, new- features, inquiries
  Plan and track releases
  Use queries (predefined or define your own)
  Use the predefined Jira Reports
  Visualize Jira project status
  Integrate Jira with Git and PullRequest

## Slide 41: Repo from GitHub

## Slide 42
Working with Git
Command Line Interface
https://git-scm.com/downloads
Source Tree GUI Client
https://www.sourcetreeapp.com/download/
https://gerrit.googlesource.com/git-repo/
https://bitbucket.sw.nxp.com/dashboard
NXP remote repo servers
Used in MCAL and OS projects

## Slide 43: Centralized Version Control System
remote repository
Anne’s working directory
Bob’s working directory
moves changes (Push)
gets changes (Pull)
gets changes (Pull)
moves changes (Push)

## Slide 44: Working with Git BASH & Source Tree
Main steps using Git Bash and Source Tree.
1. Clone the project repo. One time operation.
2. Create a branch from the JIRA ticket
3. Pull the branch
4. Checkout the branch
5. Add/update a source files
6. Commit the change
7. Pull the changes from remote repo
8. Push your change to remote repo, in the feature/ bugfix branch
9. Add a tag o the last commit form the feature/bugfix branch and push the tag
10. Merge the feature/bugfix branch to the official branch through BitBucket Pull Request

## Slide 45: Git setup on git bash
Syntax highlighting:
git config --global color.ui auto
Introduce yourself:
git config --global user.name “Name“
git config --global user.email email
Check your settings:
git config <key>
git config --list
Or check a specific key’s configuration
git clone …..
e.g. Make a clone:
Git ducation
Notes: to have syntax highlighting you can enter the first line.
in order for users to recognize your work commits, you must introduce yourself.
check your current configuration

## Slide 46
| Clone a repository
GitHub
Git Bash

## Slide 47
To clone the repo onto your local machine:
git clone <url>
Someone else’s repository can be located on their local file system or on a remote machine accessible via HTTP, HTTPS, SSH, etc.
git clone https://github.com/NXP/*repo*.git
e.g. using SSH protocol:
SSH uses public-key authentication, so you’ll have to generate one.
Cloning a repo
Notes: - you’ll need the location of your repo on the server.
- the repository hosting service used: Atlassian Stash.

## Slide 48
Now, you can notice a .git directory in the initialized project directory (is hidden).
Deleting it will turn your project into a normal unmanaged collection of files
Next, you’ll want to see the status of the repository:
git status
On branch master
Initial commit
nothing to commit (create/copy files and use "git add" to track)
Output:
random_project
.git
working directory
(files on disk)
repository
Repository status
Notes: the result of git init => a .git directory in project’s files.
running git status will show the current status of your repo.
git status will also show suggestions.

## Slide 49
Create a branch from the JIRA ticket
Notes: Go to the Jira issue you want to work on and when this issue requires modification of the data (source code, documentation etc.) stored under Git version control you should create appropriate Branch related to this issue.

## Slide 51
Committing the snapshot
Note that git status only shows the uncommitted changes.
If you run it after a commit, it will show that you have no more files to commit. (only if you don’t add new files in your working directory in the meantime)
git commit -m "Added the module definitions and functionalities"
-m flag prevents the additional editor window message to pop up.
Your message should, however, be explicit enough to others.
To exit and save contents, hit Esc and then, enter :wq.
Committing files
Notes: commit your changes, write an explicit message for the specific commit.
check commit history

## Slide 52
Checkout <branch>
To return to the current (default) branch – master (restores current files in index and working directory):
git checkout master
git checkout <branch-name>
Notes: switches you on the specified branch (e.g. switch on master => head -> master)
the detached head appears only when you check out commits, as the head no longer points to your most recent commit.

## Slide 53
Notes: switches you on the specified branch (e.g. switch on master => head -> master)
the detached head appears only when you check out commits, as the head no longer points to your most recent commit.

## Slide 54
Notes: switches you on the specified branch (e.g. switch on master => head -> master)
the detached head appears only when you check out commits, as the head no longer points to your most recent commit.

## Slide 55: ENVIRONMENT SET-UP

## Slide 56: Install VirtualBox
Prerequisites
  40 GB free space on disk
  Enable Virtualization. If is disabled, please search on google the procedure specific for your own laptop ( e.g. search on google How to Enable Virtualization on HP Latitude xxx) - Usually this is activated by default on most models.
Install VirtualBox - v7 is required
Download VM image - Eat-Sleep-Code-Repeat.ova
Eat-Sleep-Code-Repeat.ova - Google Drive

## Slide 57: Import Image into VirtualBox
Start VirtualBox
Go to File->Import Appliance… menu ( Ctrl+I)
Browse and select the downloaded Eat-Sleep-Code-Repeat.ova

## Slide 58: Import Image into VirtualBox
Select Eat-Sleep-Code-Repeat and then press Start button
Default username: student
Default password: student

## Slide 59: Import Image into VirtualBox

## Slide 60: Activate S32DS
Start S32 Design Studio for S32 Platform 3.5
Open terminal in /home/student/NXP/S32DS.3.5
sudo ./s32ds.sh
Design : Product Download : Files
If it asks for an activation code, ask for it!

## Slide 61: How Hardware and Software are Linked

## Slide 62: What is Hardware and Software?
Software refers to the set of instructions, programs and data that run on hardware, guiding it to perform specific tasks. Unlike hardware, software is intangible; it cannot be physically touched but it plays a crucial role in controlling and managing the hardware.
Hardware
Software
Hardware refers to the physical, tangible components of a computing system or electronic device. It includes all mechanical, electronic, and electric part that form the foundation of the system's functionality. Essentially, hardware is everything you can touch and see in a computer or device.

## Slide 63: From source code to executable
Compiling
Source Code
Preprocessor
Compiler
Assembler
Linker
Preprocessed file (.i file)
Assembly code (.s file)
Object code (.o file)
Executable

## Slide 64: Writing to Flash memory
Flashing the microcontroller
Microcontroller initialization
Analysis of the ELF file
Writing in FLASH memory
Memory check
Completion of the process
Connect to microcontroller

## Slide 65: S32K144 board ON VM
Set-up debug configuration & exercise

## Slide 66: S32K144
Get to Know Your Evaluation Board
02

## Slide 67: Attach Board to VM
Option 1: With VM turned OFF, select the VM and click on Settings button or press Ctrl+S keys
Select USB node then click on Add new USB filter... And from the list select PE Microcomputer Systems Inc….. device
Option 2: With VM running, from the right-bottom of the VM screen, right click on USB icon and select PE Microcomputer Systems Inc….. device from the list

## Slide 68: Create DEBUG Configuration
Start S32 Design Studio for S32 Platform 3.5
Select hello world project
Build project – click Project > Build All (Ctrl+B)
Click Run > Run or Run > Debug.
Expand GDB PEMicro Interface Debugging
If there is no entry like {project_name}_Debug_FLASH create a new configuration -> right click on GDB PEMicro Interface Debugging -> New Configuration

## Slide 69: Create DEBUG Configuration
In the Main tab select Project and C/C++ Application
In the Pemicro Debugger tab set Interface, Port
Click on Select Device and select S32K144WF512M8 device
Click on Debug button – the project will be flashed on board and the application will start to run on this.
From this point, the Debug perspective will be opened and the execution will stop at the first line of main function – click F8 to resume the code execution

## Slide 70: Exercise: RED-YELLOW-BLUE
The initial demo project will make the RGB LED to blink rapidly RED and GREEN colors
Scope of this exercise is to make the RGB LED to blink on RED, YELLOW and BLUE
RGB_BLUE – PTD0 ; RGB_RED – PTD15 ; RGB_GREEN – PTD16
Board pinout

## Slide 71: Exercise: RED-YELLOW-BLUE
Before
Target result